## Slide 1: Simulation on photovoltaic device
Presented by
Rahul Pal
Roll no- 308036
Registration No. VB-829 2021-22
Under supervision of
Dr. Swapan K. Mandal
26th May 2023

## Slide 2: Table of Contents
Introduction
Solar Cell Physics
Methodology
Results and Discussion
Conclusions
Acknowledgement

## Slide 3
Solar cell is an electrical device which converts the solar energy (energy obtained from the sun) directly into electrical energy.
Principle: The solar cells are based on the principles of photovoltaic effect.
Introduction

## Slide 4
First Generation:
Silicon wafer solar cells are the most widely used of all solar cells.
They are also the most efficient in terms of single cell photovoltaic devices, and it is the second most abundant element on Earth.
Second Generation:
Thin film solar cells emerged due to their lower production costs and minimal material consumption.
The semiconductor material used in the cell has a direct band gap as opposed to the indirect band gap of silicon.
Third Generation:
Third-generation solar cells (SCs) are solution processed SCS based on semiconducting organic macromolecules, inorganic nanoparticles or hybrids.
Common third-generation systems include multi-layer ("tandem") cells which help in minimizing energy losses in the band gap.
Solar
Cells
1st
generation
Multi
Crystalline
Silicon
2nd
Generation
Amorphous
Silicon
3rd
Generation
CIGS
CdTe
DSSC
Organic PV
Quantum Dot
PV
Perovskite
Single
Crystalline
Silicon

## Slide 5: Perovskite solar cell
Perovskite derives its name from the mineral structure Calcium Titanium oxide, discovered by German mineralogist Gustav Rose in 1839.
The special structure of this mineral was later characterized by Russian mineralogist Lev. A. perovski, thus the name.
Chemical formula of perovskite in ABX3
A = Cation
B = Metal ion
X = Anions as Oxygen,
Halogens, or alkali metals

## Slide 6
Source : https://www.nrel.gov/pv/cell-efficiency.html

## Slide 7
Easy fabrication methods
Small and tuneable bandgap
High extinction coefficient
High carrier mobility
High absorption coefficient
Advantage
Disadvantages
Pb toxicity
Stability issue
Scaling issue

## Slide 8
Solar cell parameters
Efficiency is the most commonly used parameter to compare the performance of one solar cell to another.
Efficiency is defined as the ratio of energy output from the solar cell to input energy from the sun. The efficiency of a solar cell is determined as the fraction of incident power that is converted to electricity.
Solar Cell Efficiency (PCE%)
The FF is defined as the ratio of the maximum power from the solar cell to the product of Voc
Fill factor (FF)
Where: Voc is the open-circuit voltage; Isc is the short-circuit current; FF is the fill factor and η is the efficiency.

## Slide 9
Open-circuit voltage (VOC )
The open-circuit voltage,, is the maximum voltage available from a solar cell, and this occurs at zero current.
The short-circuit current is the current through the solar cell when the voltage across the solar cell is zero.
Short-Circuit current ( Jsc)
The "quantum efficiency" (Q.E.) is the ratio of the number of carriers collected by the solar cell to the number of photons of a given energy incident on the solar cell.
Quantum efficiency

## Slide 10
The device structure, related materials, and interfacial modification are key factors in performance of solar cells.
Electron transport layer (ETL) is used to collect & transport the electrons.
Hole transporting layer (HTL) is used to collect & transport the holes.
Perovskite solar cell device structure
Schematic diagram of Perovskite Solar cell

## Slide 11
Methodology
Using the SCAPS-1D simulation programme, the perovskite solar cell characteristics were designed and analysed in the current work . The devices in our investigation are simulated using SCAPS-1D software.
In this cell structure, Light beams fall on indium tin oxide (ITO), which serves as a front contact. The n-type Tungsten disulphide (WS2) contacts that are formed on ITO serve as an electron transport layer. A layer of 3-hexylthiophene-2,5-diyl (P3HT), which is used as the HTL, is placed above the perovskite methyl ammonium lead iodide (CH3NH3PbI3) and serves as an absorber layer.

## Slide 12
To achieve their maximum values and to enhance the performance of perovskite solar cells, the simulation method adjusted the characteristics of PV cells including thickness, band gap, acceptor density, and absorber temperature while holding all other factors constant.
What do with SCAPS 1D ?
Influence of variation in thickness of absorber layer
Effect of variation in the bandgap of absorber layer on device parameters
Impact of variation in doping concentration of absorber layer
Influence of varying temperature on solar cell parameters

## Slide 13
SCAPS-1D simulator used show the input panel to start defining the solar cell different layers.

## Slide 14
Here SCAPS-1D simulator used to calculate these recorded data.

## Slide 15
Result and Discussion
The simulation results imply as perovskite thickness varies,
PCE increases and becomes maximum at 1.3 μm absorber (CH3NH3PbI3 ) thickness.
VOC goes up rapidly with the increasing thickness of the perovskite layer.
JSC increases on increasing thickness of CH3NH3PbI3 absorber.
fill factor (FF) decreases when the thickness of an active layer increases due to an increase in series resistance.

## Slide 16
The simulation results imply as perovskite bandgap varies,
PCE decreases as the bandgap increases increasing the bandgap lowers the number of photons that are absorbed while raising the energy .
VOC has an ideal value when the bandgap is between 1.5–1.7 eV and later on, as the material's bandgap is increased, it somewhat reduces.
JSC steadily decreases as the bandgap increases, the higher energy photons' absorption decreases.
The FF increases on increasing band gap to 1.95 eV

## Slide 17
The gained PCE of the photovoltaic cell at 1 × 1013 cm−3 is 26.788% and 29.73% at 1 × 1022 cm−3 after that on increasing doping concentration.
The maximum VOC is obtained as 1.5907 V at 1 × 1022 cm−3.
JSC is found to be 23.795 mA cm−2 at 1 × 1013 cm−3 and decreases to 20.22 mA cm−2 at 1 × 1022 cm−3.
FF is constant up to 1 × 1015 cm−3 and after that abruptly rises up to 1 × 1021 cm−3
The acceptor concentration was varied from 1 × 1013 cm−3 to 1 × 1022 cm−3

## Slide 18
Usually, in this simulation work, the temperature has been set from 250 K–300 K to see how raising the operating temperature affects the cell’s performance
PCE decreases with the increasing in the operating temperature. At operating temperatures of
250 K—300 K efficiency of 27.84% to 26.78% are obtained .
VOC falls abruptly from 1.29 V to 1.26 V with the increasing in operating temperature.
JSC increases on increasing temperature.
FF decreases from 90.57% to 89.129% with the increasing in operating temperature

## Slide 19
Final Outcome
The simulation resulted in a Power Conversion Efficiency (PCE) of 28.38%, short-circuit current density (JSC) of 21.86 mA cm−2, fill factor (FF) of 90.93% and an open-circuit voltage (VOC) of 1.4275 V.
The simulation resulted maxima shows the current density and voltage characteristics, as well as the quantum efficiency (QE) curve.

## Slide 20
Conclusion
The studied perovskite solar cell has the highest efficiency of 28.38%. Perovskites with a bandgap of 1.6 - 1.7 eV should be employed as an active layer to achieve good photovoltaic performance.
The simulation study of lead-based CH3NH3PbI3 perovskites solar cells shows that the performance of the device highly depends on the thickness of the absorber layer, work function and various parameters such as defect density, doping density of acceptor and donor atom and temperature.
My simulation analysis demonstrates that the suggested design might be used to create a device for enhancing the effectiveness of the perovskite solar cell.

## Slide 21
We are thankful to Dr. Burgelman and his team, the Department of Electronics and Information Systems University of Gent Belgium for developing SCAPS -1D tool.
I express my deep gratitude, regard to my supervisor, Dr. Swapan Kumar Mandal, for his constant encouragement and valuable suggestions. I would have made no progress without his help and support.
I would like to convey my heartfelt gratitude to Paramesh Chandra (Ph.D. Scholar, Visva-Bharati), my mentor, for his invaluable advice and assistance in completing my project. I thank my classmate Saikat Samadder for his assistance in different ways.
I am really grateful to my family for their constant support and encouragement.
Acknowledgments

## Slide 22
Thanks for listening
Thanks for giving me the place to work and identify with